## Slide 1: PA Fluoroscopy
Digital Fluoroscopy

## Slide 2
Matrix – grid made of pixels
Pixel – picture element
SNR / CNR
CCD – Charge coupled device
PACS – Picture Archival and Communication System
HIS / RIS
HIPAA
Terminology

## Slide 3: Terminology
Flat panel detector
Contrast resolution / Dynamic range
DICOM gray-scale function
WW/WL function
DSA
Sampling frequency
DEL (detector element size)

## Slide 4: Matrix
Every image is made of small squares called pixels (picture element)
Within a specified field size, an increased matrix will equate to a more detailed image
  Let’s say we have a 9” square field
  If the field has a matrix of 16 x 16, the pixels are large
  If the same field has a matrix of 512 x 512, the pixels are considerably smaller

## Slide 5
http://www.picturemosaics.com/gallery/zoom.php?i=30&rows=4&page=2&term=

## Slide 6
Would be used instead of a TV camera at the output phosphor
Mounted on the output phosphor, the light is transferred through fiberoptics
The sensitive layer of the CCD is composed of crystalline silicon
Charge Coupled Device

## Slide 7: Charge Coupled Device (cont)
When the silicon is illuminated, an electrical charge is generated
Electrical charge is put through the ADC (analog-to-digital converter) then sent to the computer

## Slide 10
The CCD contains pixels arranged in a matrix
Each pixel is sampled and manipulated to produce a digital image
No lag or blooming
No spatial distortion (pincushion)
Charge Coupled Device (cont)

## Slide 11: Charge Coupled Device (cont)
No warm up time
Lower patient dose
Image quality depends on the matrix of the CCD

## Slide 13
Flat Panel Image Receptor (FPIR)
Used in place of an image intensifier
Composed of CsI / a-Si detector elements (DEL)
  Each DEL represents a pixel
  Size of the pixel will help determine spatial resolution
Pixel size = FOV divided by matrix
Flat Panel Detector

## Slide 16: FPIR
Digital fluoroscopy operates in radiographic mode
  Tube current measured in hundreds of mA instead of 1 to 5 mA
Images are obtained in a manner called pulse-progressive fluoroscopy
Imaging rates between 1 and 10 frames per second

## Slide 17: FPIR (cont)
Exposures can be continuously varied for dose reduction
Each time the flat panel is exposed, it is read immediately and the image is projected until the next image is acquired
X-ray generator must be capable of switching on and off very rapidly

## Slide 18: FPIR (cont)
Interrogation time is the time required for the x-ray tube to be switched on and reach selected levels of kVp and mA
The time required for the x-ray tube to be switched off is the extinction time
HF generators are used to keep interrogation and extinction times (total on/off cycle) to less than 1 ms

## Slide 19: FPIR (cont)
The fraction of time the tube is energized is the duty cycle
The next graphic shows the x-ray tube is energized for 100 ms every second
This represents a 10% duty cycle
Can result is significant dose reduction

## Slide 22
Higher DQE than CCD
Distortion-free images
Improved contrast resolution
  The ability to distinguish many shades of gray from black to white
  Grayscale (dynamic range)
A rectangular image area can be matched with a rectangular display
FPIR Quality

## Slide 23
Typical imaging chain in conventional fluoroscopy
X-ray tube is below table
Light from x-ray photons are “intensified” through the image intensifier
Light at the output phosphor is split between a TV monitor and a recording device
Conventional vs. Digital

## Slide 25
Typical components of a digital system
Instead of a TV camera attached to the output phosphor, a CCD or flat panel is used
A computer is used to allow manipulation of images
Brightness of the image is based on the pixel values
Conventional vs. Digital

## Slide 28
SNR – Signal to Noise Ratio
  Signal from the unit scaled against inherent noise of the system
  1000:1 is needed in DF
SNR / CNR

## Slide 29: SNR / CNR (cont)
CNR – Contrast to Noise Ratio
  Relationship of signal intensity differences between two regions scaled to image noise
  Increased CNR increases perception of distinct differences between two areas
  Both pertain to video display

## Slide 30
Typical display monitors (CRT) with interlaced mode (525 lines per frame consisting of two fields of 262.5 lines each)
Interlacing action of a display degrades the image
Television cameras are noisy
SNR is about 200:1
Video Display

## Slide 31: Video Display (cont)
DF TV camera tubes reads in progressive mode
  Video signal sweeps from top to bottom in 33 ms
There may not be a TV camera if the signal goes to the computer first
No flickering
Sharper image

## Slide 32
Many systems use flat panel displays
Easier to view and easier to manipulate
Better image quality
Lightweight and easy to see
Can be suspended from the ceiling
Digital imaging allows image manipulation
Video Display (cont)

## Slide 33
Most common method of image manipulation
Dependent on bit depth of the system
  Bit processing will determine how many shades of gray can be manipulated
  For instance, an 8-bit system would have 256 shades available while a 10-bit system would have 1024
Window and Level

## Slide 34
Contrast in different regions of interest can be enhanced as long as the computer system has a sufficient dynamic range
With digital, we can alter the display window and level
  Window is the number of gray shades (controls image contrast)
  Level (center) is where that window is centered along the gray scale (controls image brightness)
Window and Level (cont)

## Slide 36
Digital Subtraction Angiography
Helps enhance image contrast through post-processing
Steps involved include creating a mask, applying an image with IV contrast, and subtracting out the information that is not needed
DSA

## Slide 39
This is an example of misregistration artifacts. Typically happens when the patient moves between the mask image and a subsequent injected image. The subtraction image contains the artifacts.

## Slide 40: Roadmapping
A special application of DSA
The mask image is stored, contrast is injected, and subtracted images are acquired
As the catheter is advanced, another mask is obtained showing the catheter in the vessel

## Slide 41
Roadmapping

## Slide 42
Picture Archival & Communication System
Allows acquisition, interpretation, and storage of images
Four components: acquisition, display, network, and storage
Separate from any other network in the facility
PACS

## Slide 43
PACS can accept any image in a DICOM format
Digital Imaging and Communications in Medicine
DICOM is a standard
Prior to that, each vendor had its own way of storing images with no need to share
DICOM

## Slide 44
Each manufacturer has its own proprietary image file which needs to be converted into DICOM
Within the image file, there are other pieces of information like patient and image information
DICOM is an object-oriented standard
  Two classes of information
DICOM (cont)

## Slide 45
Object class
  Contains information about the study and the patient
  Includes normalized and composite information
Service class
  Describes what to do with the object
  Includes image storage, image query, image retrieval, image print, storage resource, and composite information
DICOM (cont)

## Slide 46
HIS: Hospital Information System
  Holds a patient’s full medical record (billing, inpatient ordering)
RIS: Radiology Information System
  Holds radiology-specific patient data (patient scheduling, reports)
EMR: Electronic Medical Record
EHR: Electronic Health Record
HIS / RIS / EMR

## Slide 47
HL 7: Health Level 7
Oversees most clinical and administrative data
  Demographics, reports, claims, orders (text based information)
  A standard generally used to communicate between the HIS and RIS
HL 7 Standard

## Slide 48
Stands for the Health Insurance Portability and Accountability Act of 1996
Mandated governing the provision of health benefits, delivery and payment for healthcare services, and security / privacy of protected health information (PHI) in written, electronic or oral formats
HIPAA